## Slide 1: A YANG Data Model for WDM Tunnels
Co-authors:
Aihua Guo (Futurewei)
Sergio Belotti (Nokia)
G. Galimberti (Individual)
J.E.L.d.V. Mendez (Naudit HPCN)
D.P. Burrero (Universidad Autonoma de Madrid)
draft-bgk-ccamp-merged-wdm-tunnel-00
Contributors:
Daniel King (Olddog Consulting)
Haomian Zheng (Huawei)
Italo Busi (Huawei)
Victor Lopez (Nokia)
Dieter Beller (Nokia)
Ricard Vilalta (CTTC)
Young Lee (Samsung)
Bin Yeong Yoon (ETRI)
Daniel Michaud Vallinoto (Universidad Autonoma de Madrid)
Zafar Ali (Cisco)
IETF 118, Prague

## Slide 2: Motivations
Currently there are two separate WG drafts on WDM-related tunnel models
  draft-ietf-ccamp-wson-tunnel for WSON fixed-grid wavelength switched optical networks
  draft-ietf-ccamp-flexi-grid-tunnel for flexi-grid elastic optical networks
Technology migration towards mixed WSON/flexi-grid optical networking
  The YANG model needs to support scenarios where fixed-grid and flex-grid switches may co-exist in operator’s networks
  Shared definitions and model constructs between WSON and flexi-grid
WG consensus to merge the two tunnel models into one common model
A
Z
WSON
GMPLS Domain
Flexi-grid
GMPLS Domain

## Slide 3: Logistics for Merging
Create this new I-D, draft-bgk-merged-wdm-tunnel-00
Asking WG to adopt it and replaces the two old WG drafts
And…keep improving the draft following WG procedures

## Slide 4: -00 Draft Update
Updates to the text description to reflect a unified view of WDM tunnel models
  The scope of this draft is to define data models for WDM tunnel provisioning in WSON, flexi-grid network or a mix of both networks
Updates to the YANG model
  Combined WSON and flexi-grid label-related structures (label-start-end, label-step, label-range, etc.)
  Support both the integrated scenario and book-ended (OLS + external transponder, POI) scenario
  Intending to reuse the same common grouping between WDM tunnel and optical path computation
Updates to RFC9093-bis
  Adding common WDM groupings
Added new parameters to allow client to indicate WDM technology-specific constraints to influence path selections and WDM tunnel behaviour
  Transceiver specification (both tunnel- and path-scope), e.g. transceiver’s operational mode
  Optical impairment / performance, e.g. G-SNR margin
  WDM path constraints, e.g. wavelength conversion, regeneration, transceiver retuning

## Slide 5: Transceiver Specifications
Unified transceiver specifications for both integrated and OLS / POI scenarios
Inverse multiplexing for 400G and above
Transceiver specifications aligned with draft-ietf-ccamp-optical-impairment-topology
augment /te:te/te:tunnels/te:tunnel:
+--rw wdm-constraint
+--rw transceiver-constraint
| +--rw operational-modes* string
| +--rw tx-tune-constraints
| +--rw min-central-frequency? frequency-thz
| +--rw max-central-frequency? frequency-thz
| +--rw transceiver-tunability? frequency-ghz
Tunnel-scope
augment /te:te/te:tunnels/te:tunnel/te:primary-paths
/te:primary-path/te:explicit-route-objects-always
/te:route-object-exclude-always/te:type
/te:numbered-node-hop/te:numbered-node-hop:
+--rw path-in-transceiver
| +--rw transponder-id? uint32
| +--rw transceivers* [lane-id]
| | +--rw lane-id uint8
| | +--rw transceiver-id? uint32
| +--rw operational-modes* string
| +--rw tx-tune-constraints
| +--rw min-central-frequency? frequency-thz
| +--rw max-central-frequency? frequency-thz
| +--rw transceiver-tunability? frequency-ghz
+--rw path-out-transceiver
+--rw transponder-id? uint32
+--rw transceivers* [lane-id]
| +--rw lane-id uint8
| +--rw transceiver-id? uint32
+--rw operational-modes* string
+--rw tx-tune-constraints
+--rw min-central-frequency? frequency-thz
+--rw max-central-frequency? frequency-thz
+--rw transceiver-tunability? frequency-ghz
Path-scope

## Slide 6: WDM Label Specifications
WSON
  DWDM fixed-grid and CWDM
Flexi-grid
Single vs. Multi-carrier
augment /te:te/te:globals/te:named-path-constraints
/te:named-path-constraint
/te:explicit-route-objects-always
/te:route-object-include-exclude/te:type/te:label
/te:label-hop/te:te-label/te:technology:
+--:(wdm)
+--rw (grid-type)?
+--:(fixed-dwdm)
| +--rw (fixed-single-or-super-channel)?
| +--:(single)
| | +--rw dwdm-n? l0-types:dwdm-n
| +--:(multi)
| +--rw subcarrier-dwdm-n* l0-types:dwdm-n
+--:(cwdm)
| +--rw cwdm-n? l0-types:cwdm-n
+--:(flexi-grid)
+--rw (single-or-super-channel)?
+--:(single)
| +--rw flexi-n? l0-types:flexi-n
| +--rw flexi-m? l0-types:flexi-m
x--:(super)
| +--rw subcarrier-flexi-n* [flexi-n]
| +--rw flexi-n l0-types:flexi-n
| +--rw flexi-m? l0-types:flexi-m
+--:(multi)
+--rw frequency-slots
+--rw frequency-slot* [flexi-n]
+--rw flexi-n l0-types:flexi-n
+--rw flexi-m? l0-types:flexi-m

## Slide 7: WDM Constraints for Path Selection
Same constraints definition reused for optical path computation
+--rw gsnr-margin? snr
+--rw use-regen? boolean
+--rw wavelength-conversion? boolean
+--rw bit-stuffing? boolean
+--rw wavelength-assignment? identityref
+--rw guard-band-size? l0-types:frequency-thz
+--rw matching-fwd-rev-wavelength? boolean
+--rw allow-retuning? boolean
+--rw delta-power? l0-types:gain-in-db-or-null

## Slide 8: Next Steps and Actions
Request WG adoption to replace the WSON and flexi-grid tunnel draft
Align the model between this draft and draft-ietf-optical-path-computation
Address remaining open issues for WSON and flexi-grid tunnel
Support the association of a WDM tunnel with management objects, e.g. media channels, OTS/OMS path
  Weekly team meeting:
    Thursday, 14:00 (CET)
    CCAMP WebEx Details
      https://ietf.webex.com/ietf/j.php?MTID=ma1ca3bcec716fe1ff93e0a28b3558294
      Join by meeting number
        Meeting number (access code): 2422 698 1495
        Meeting password: 6UbM2tEJJd6

## Slide 9: Backup Slides

## Slide 10: WDM Tunnel and MC
A
Z
WSON
GMPLS Domain
Flexi-grid
GMPLS Domain
WDM Tunnel
- primary path (nominal)
- primary path (active)
- secondary path (nominal)
- secondary path (active)
Media channel (management layer)
- primary MC connection (active)
- secondary MC connection (active)